## Slide 1
Low-Cost AI-Based Semiconductor Defect Detection System Using Computer Vision
Final Year B.Tech Capstone Project Proposal
Guide: Dr. Subhasish Mahapatra
Student: [Sujal Kumar (23BEC7061) Dania Firdoush(23BEC7084) ] Department: Electronics & Communication Engineering SENSE
Academic Year: 2023–27
COMPUTER VISION
DEEP LEARNING

## Slide 2
Problem Statement & Motivation
The Inspection Challenge
Semiconductor fabs require 100% wafer inspection — even microscopic defects cause chip failure
Manual inspection is slow, costly, and error-prone under high-volume production
Industrial AOI systems cost $50K–$500K, inaccessible to SMEs and research labs
Core Gap: No affordable, automated, AI-driven inspection solution exists for low-resource environments.

## Slide 3
Proposed Solution: AI-Based Defect Detection System
An end-to-end automated pipeline combining CNN-based classification with a web monitoring dashboard — deployed on existing hardware at near-zero cost.
Web Dashboard
Defect Classify
CNN Preprocess
Wafer Input
The system accepts wafer map images or live camera input, processes them through a trained CNN, and outputs defect type, confidence score, and severity rating via a browser-based interface.

## Slide 4
System Architecture
Architecture Highlights
Input Layer: WM811K dataset or USB camera feed (256×256 grayscale)
Preprocessing: Normalisation, data augmentation, noise filtering via OpenCV
CNN Core: 4 convolutional blocks with max-pooling and dropout regularisation
Output: 7-class softmax with confidence thresholding and severity flagging

## Slide 5
Dataset & Defect Categories
The WM811K Wafer Map Dataset (Kaggle) contains 811,457 labelled wafer maps across 7 defect patterns — the benchmark for semiconductor ML research.
Normal
No defects detected
Center
Defects clustered at wafer center
Donut
Ring-shaped defect distribution
Edge Ring
Defects along wafer perimeter
Scratch
Linear mechanical damage marks
Near Full
Near-total wafer coverage
Random
Scattered, uncorrelated defects

## Slide 6
AI Model Design: CNN Architecture
Model Specifications
Input: 256×256 grayscale wafer map images
Feature Extraction: 4× Conv2D blocks (32→64→128→256 filters)
Regularisation: MaxPooling2D + Dropout (0.5)
Classification: Dense(128, ReLU) → Softmax(7)
Tools: Python 3.10, TensorFlow 2.x, Keras, OpenCV
Target accuracy: >95% on WM811K test set

## Slide 7
Software & Hardware Requirements
Software Stack
Tool
Purpose
Python 3.10
Core language
TensorFlow 2.x
CNN model training
OpenCV
Image preprocessing
Flask
REST API backend
React.js
Web dashboard UI
Hardware
Component
Specification
Laptop (existing)
Intel i5 / 8 GB RAM
Storage
SSD (dataset ~2 GB)
USB Camera (opt.)
5 MP, ₹800–₹1,000
Internet
For dataset & libraries
All software is open-source and free. No dedicated GPU required.

## Slide 8
Cost Analysis & Feasibility
Budget Breakdown
Item
Cost (₹)
Existing Laptop
₹0
WM811K Dataset
Free
Software Tools
Free
USB Camera (optional)
₹800–₹1,000
Total Estimated
₹0–₹1,000
Feasibility Assessment
✅ Technically Feasible
Proven CNN architectures on public dataset; open-source toolchain
✅ Financially Feasible
Near-zero capital expenditure; leverages existing institutional hardware
✅ Academically Suitable
Integrates ECE, AI, and embedded systems — ideal for final-year scope

## Slide 9
Expected Results & Industry Applications
System Outputs
Defect Type
One of 7 WM811K classes
Confidence Score
Softmax probability (%)
Severity Flag
Pass / Monitor / Reject
Target classification accuracy: >95% on held-out test data
Industry Relevance
Directly applicable to semiconductor manufacturers seeking cost-effective inline inspection:
Intel · AMD · NVIDIA
High-volume fab defect screening
Qualcomm · Micron
Mobile & memory device QA
Semiconductor Fabs
SME and research lab deployment

## Slide 10
Conclusion & Future Scope
Project Summary
Low-cost, AI-driven wafer inspection system — under ₹1,000
Converges ECE, Computer Vision, Deep Learning, and Industry 4.0
Deployable on existing hardware with open-source tools only
Addresses a real industrial gap in affordable automated inspection
CAPSTONE-READY
IEEE-ALIGNED
Future Roadmap
01
Real-Time Camera Inspection
Live wafer feed with sub-second inference
02
Raspberry Pi Edge Deployment
Portable, low-power inline inspection unit
03
FPGA Acceleration
Hardware-level inference speed-up for production fabs
04
Industrial-Scale Pilot
Collaboration with semiconductor manufacturing partners